## Slide 1
RISC-V Trace Verification: Block Level CoCoTb based Verification in Shakthi C-Class Processor
UG PROJECT 2025-26
EC22711 - Project Work Phase - I Viva-Voce
Supervisor
Mr. Silambarasan D
Assistant Professor
Department of ECE
Members of students: (C21)
Srinath S (No.: 2127220701138)
Vijai Saravanan R G (No.:2127220701160)

## Slide 2: Problem Statement
• Traditional verification focuses only on the final output correctness of processor execution.
• A processor may still produce the correct output even when the internal instruction execution sequence is incorrect.
• Such hidden deviations can cause undetected bugs in:
1. Branch and control-flow execution
2. Privilege mode transitions (U/S/M)
3. CSR operations and system control behavior
4. Trap/exception handling
• Debugging becomes difficult without visibility into the actual execution path.
• There is a need to verify the instruction-by-instruction execution flow of Shakti C-Class to ensure strict compliance with the RISC-V ISA and Privileged Specifications.

## Slide 3: Proposed Solution
• Develop a block-level trace verification methodology for Shakti C-Class RISC-V processor.
• Use CoCoTb, a Python-based verification framework, to monitor internal RTL signals during execution.
• Capture the Program Counter (PC) trace for every executed instruction.
• Compare the logged execution trace against:
1. Expected flow from disassembly
2. Reference behaviour validated using Verilator
3. RTL generated dump trace
• Detect missing, skipped, or misaligned instruction events and analyze trace visibility gaps.

## Slide 4: Objectives
• To design and implement a CoCoTb-based block-level trace verification environment for Shakti C-Class RISC-V processor.
• To capture and log PC traces during RTL simulation of RISC-V assembly test programs.
• To validate instruction execution flow against the RISC-V ISA and Privileged Architecture specifications.
• To identify and analyze missing or untraced instruction patterns across multiple RISC-V test suites.
• To build a trace verification methodology that acts as a foundation for full core-level and data-trace verification.

## Slide 5: Why RISC-V and Shakti C-Class?
Why RISC-V?
• Open-source Instruction Set Architecture (ISA) with no licensing cost.
• Modular and extensible design → supports custom extensions for research and industry.
• Widely adopted for academia, embedded systems, IoT, and processor R&D.
• Scalable architecture supporting standard extensions such as I, M, A, F, D, C.
• Enables transparent verification and open-source hardware development.

## Slide 6: Why RISC-V and Shakti C-Class?
Why Shakti C-Class?
• Developed by IIT Madras as part of India’s open-source processor initiative.
• 64-bit RV64IM core suitable for mid-range embedded and IoT applications.
• Supports User, Supervisor, and Machine modes as per RISC-V Privileged Spec.
• Includes integrated debug and trace support required for verification and validation.
• Strengthening Shakti verification contributes to India’s indigenous semiconductor ecosystem.

## Slide 7: RISC-V Execution Modes
Execution Modes:
1. Machine Mode (M-Mode):
Full-access mode used for system control and boot.
2. Supervisor Mode (S-Mode):
OS mode that manages memory and system protection.
3. User Mode (U-Mode):
Application mode with limited access for safety.
Why It Matters in Verification:
Execution modes ensures secure and correct switching between modes.

## Slide 8: Shakti C-Class Architecture

## Slide 9: What is Trace Verification
Trace Verification
• A verification technique that validates the exact sequence of instructions executed by the processor.
• Ensures that the processor follows the correct architectural flow, not just the correct final output.
• Helps detect hidden design bugs that may not reflect in output-based verification.
Why is it Important?
A processor may produce the correct final result even when internal execution steps are wrong.
Identifies issues in:
• Branch and jump execution
• Pipeline flush and control-flow handling
• CSR operations and privilege mode transitions
• Trap/exception entry and return sequences

## Slide 10: Instruction Trace
• Instruction Trace ensures the processor follows the correct architectural execution flow as defined by the RISC-V ISA.
• It validates the Program Counter (PC) sequence to confirm proper control-flow throughout program execution.
• Enables detection of subtle internal design issues that may not appear in output-based verification, such as:
• Missing or untraced instructions
• Incorrect branch/jump behaviour
• Unauthorized privilege level changes
• Missed traps or CSR operations
• Traced PC values from RTL simulation are compared against the expected flow obtained from the program disassembly.

## Slide 11: Workflow

## Slide 12: Trace Components
Trace Encoder
• Hardware block that captures instruction execution information.
• Records key details like PC values for trace visibility.
Trace Packet
• Trace data is compressed into small packets for efficient storage/transfer.
• Helps in reconstructing the execution flow later.
Trace Decoder
• Software/logic that reads and interprets trace packets.
• Rebuilds the instruction sequence for verification and analysis.

## Slide 13: PC Trace Capture in CoCoTb
During simulation, the PC value is obtained by referencing the trace ingress signal within the RTL hierarchy using the following CoCoTb handle:
dut.soc.soc.ccore_0.riscv_etrace_ingress_port_iaddr.value
Table: Signal Hierarchy Used to Access PC:

## Slide 14: CoCoTb Result

## Slide 15: Missing Instruction
Missing Instruction Analysis – ADDW Test
• Some instruction addresses in the disassembly were not captured in the trace log.
• Missing PCs were mapped to their corresponding assembly instructions.
• These instructions executed correctly but were not traced, showing trace visibility gaps

## Slide 16: Final Analysis of I-Trace [Results]

## Slide 17: References
[1] RISC-V Foundation, The RISC-V Instruction Set Manual, Volume I: Unprivileged ISA, Version 20191213, pp. 1–229, 2019.
[2] RISC-V Foundation, The RISC-V Privileged Architecture Specification, Version 1.12, pp. 1–141, 2021.
[3] Shakti Project, C-Class Core Documentation, Indian Institute of Technology Madras, India, 2024.
[4] Vyoma Systems, Industrial Verification Framework for Shakti Processors, Technical Documentation, Vyoma Systems Pvt. Ltd., Bengaluru, India, 2025.
[5] CoCoTb Developers, CoCoTb: Coroutine-based Co-Simulation Testbench, Version 1.8, pp. 1–96, 2024.
[6] GNU Project, RISC-V GCC Toolchain Documentation, Free Software Foundation, Boston, MA, USA, 2024.
[7] IEEE Standard 1800-2017, IEEE Standard for SystemVerilog – Unified Hardware Design, Specification, and Verification Language, IEEE, New York, USA, 2017.
[8] D. A. Patterson and J. L. Hennessy, Computer Organization and Design: The Hardware/Software Interface, 5th Edition, Morgan Kaufmann Publishers, San Francisco, CA, USA, 2014.
[9] D. Patterson and A. Waterman, The RISC-V Reader: An Open Architecture Atlas, 2nd Edition, Strawberry Canyon LLC, Berkeley, CA, USA, 2017.